Enemy Detector Shooting Car
Group Member

Name	Roll
Md. Iftakher Ahmad	Ek-21
Md. Rajib Hossain	FH-35
Mridul Banik	JN-46

Platform
Arduino IDE

Goal:
The main purpose of our project is to shoot an enemy after detecting it. It can be used as a demo project in defense sector.

Apparatus:

1. DC motor
2. wheel
3. motor driver
4. arduino
5. transistor
6. battery
7. gear motor
8. sonar sensor
9. servo motor
10. bluetooth module
11. jumper wire
12. shooting gun
13. glue gun

Procedure:
To shoot an enemy it follows some roles such as it never shoots when it will found any motionless obstacles. It only shoot when it will get moving object in front of this shooting car. It will also stop moving when it approaches to a hole. As it is a remote control car, we can control the car using remote. If we set the remote as right then the car will move on the right side. If we set the remote as left then the car will move on the left side. Thus the car can also move forward and backward when the remote is set forth and back simultaneously. The car can also be controlled using voice. If we say ‘left’ then the car will move to the left. If we say ‘right’ then the car will move to the right. Thus the car can also move to the forward and backward when we say ‘forward’ and ‘backward’ simultaneously. When the car move to the right , the right wheels speed will be less than the right that means the right wheels will slowly move and left wheels will move fast and when the car move to the left, the left wheels will slowly move and right wheels will move fast. When the car find any obstacles in front then it will stop for a while. Then it will check whether the obstacles is motionless or movable. If the obstacle is motionless then it will check the left side as if obstacle free. If true then it will move to the left side. Otherwise it will move to the right side. Thus this procedure will continue and so on. DC motor is used for running car wheels. it’s speed and direction are controlled by motor driver. Gear motor is used for triggering gun. A transistor is used for it’s switching logically from program. Bluetooth module is used for wireless communication with controlling device. It’s RX and TX pin is connected with arduino’s TX and RX pin sequentially. Servo motor is used for moving one sonar sensor.

Special case: When the car find any hole, the car will stop and move to the free sided area.

Limitations:
This shooting car will not move at low power supply.
Shooting accuracy may be erroneous.
The bullet are loaded as manually.